## Slide 1: LCAMP Platform LCAMP Configurator DHBW-Heidenheim Prof. Dr.-Ing. Klaus-Dieter Rupp
2024-09-12

## Slide 2: Basic Specification of LCAMP Robot

## Slide 3: Issues
Sensorbox
Maximum Wheelsize 4inch about 100mm
Sid sensorboxe move alite out to outer Size 210 mm
Widht of Front Sensorbox 210mm wir 2mm Radius at the edge
Heigth of Sensorbox rised to 64mm
Chassis
Raster for holes centered with 20mm
The Chassis will be 140mm x 300m  140mm+m*40mm x  300mm+n*40mm
(for symetric centered approach)
With the center of wheelhubs 38 mm blow the top ground clearance will be 20mm -24mm
Drive Systems
Higher stability for Drive Holder  canadian solution
Drive Systems could be preassembled The Power-PCB could be placed on the Driveholder. ( screwing from the top)
The same hole for Driveholder of DC-motor and Stepper-motor
Wheels
Maximum wheelsize 4inch about 100mm  desinged wheelsize 96mm
All wheels should have the same size
The wheelbase should be 200mm
The center of the wheel hub shoud be 40mm below the top cover
The baseframe is the top of the robot
We have in case of Stepper motors 5mm axis diameter
We have in case of DC-Motors and passive holders 6mm axis diameter
Battery
Big battery with 5200mAh
Small battery with 3300mAh
Different battery connecter and charging connector including mainswitch and Power LED. Charging without dissasabling the Robot.
Controller
V1 with existing Controller for Arduino Uno-R4 and Mega
V2 Holder for Uno R4 and Mega with 90° offset

## Slide 4: Extensions
Small battery
Arduino integrated in Sensorbox
Controller with Battery
V2 Holder for Uno R4 and Mega with 90° offset including battery holder
Sensorboxes
Instead of using a I²C splitter, use a esp32, (Rapi Zero, Adruino nano) as a decentrelized Sensorbox controler.
Common Protocoll to main Controller
Pre comissioning of the Sensorbox

## Slide 5: Open Configuration Workspace
Omni Drive
Differential Drive
Stepper motor
Stepper motor
Stepper motor
DC motor
Big Battery
Small Battery
Arduino Uno R4
4 mecanum wheels
2 regular wheels
2 omni wheels
Arduino Mega
Other
US-SensorHC-SR4
Lidar-Sensor
RGB-Light
Environmental DHT22 AM2302
IR Sensor
IMU
Remote Control
MQQT, CAN
Line follower
Taktile switch
CAM Module
Sesorbox straight
Sesorbox cracked
Chassis
Acryl
Chassis
Alu
Chassis
Composit
Pasive holder
STM32
Other

## Slide 6: Structure of LCAMP Configurator
Delfined Part
Arduino Code
PartList
Robot Configuration
Robot config
Delfined Part
Delfined Part
Defined Part
Configruration for Matlab
Simumatik
Edge, Force

## Slide 7: LCAMP configurator
Workstaton Description
Robot
config Dictionary
Robot
config .excel
Robot config
.json
Robot
Config c#
Device-Description
(Assembly, ArduinoCode)
List of Materials
Robot
Config
Tree
Robot basic config
List of Parts
List of Components
List of Devices
Process Description
Microcredentials
Warehous List

## Slide 8: Structure of Robot Configuration
2
Defined Part
Description
Arduino Code
Assembly
…
Configuration Tree
Robot
SubSystem
Component A
Part 1
Part 2
…
Component B
Part1
Part

## Slide 9: User Interface V1
Base Functionality:
Definition fo Robot,
Drive-System, Wheels ,
Export for Part-List, Sensors and Controller
Using .json Templates and STL-Files

## Slide 10: User Interface V2
Extended by:
3D Graphical Representation
Color Scheme Management
Web Interface

## Slide 11: LCAMP viewer
Delfined Part
Robot Configuration
Delfined Part
Delfined Part
Defined Part
.STL File 3DPrint
.PDF File Drwawing
.XLSX File
PartList

## Slide 12: Structure LCAMP Process
Delfined Part
Assembly Structure
PartList
Logistics Configuration
Warehouse Structure
Delfined Part
Delfined Part
Defined Part
Order
Procurement
Assembly
Shipping
Production
Configuration
Assembly

## Slide 13: Structure
Configuration Tree
  Assembly
    Warehouse
      Package
        Assembly
        Assembly
    SubSystem
      Component A
        Part 1
        Part 2
        …
      Component B
        Part1
        Part 2
Assembly: Quantity of unassembled parts
Warehouse: A Location where assemblies are stored
Package: A bundle of Assembly's or Parts
Sub-System: Assembled System or Subsystem including Electronics or Software
Component: Assembled Structure without System Behavior (eg. Wheel)
Part: Single Part
Device: Part with electronic functions
For Order you can have:
  Assembly
    Package
      Assembly
      Assembly

## Slide 14: Order Processing
https://simpleclub.com/lessons/bueromanagement-prozess-der-auftragsbearbeitung
https://www.jh-profishop.de/profi-guide/auftragsabwicklung/?srsltid=AfmBOoqKC_osTfEmkGwEeMSAm6I2ofYC_VqPU17LB9zdT8l__v2NmVrk
https://www.atlassian.com/de/work-management/knowledge-sharing/documentation/process-documentation
Order receipt
Order entry
Order processing
Shipping preparation & shipping
Invoicing

## Slide 15: Process Configurator

## Slide 16: Order Processing Tool

## Slide 17: Process Configuration
Sub Process
Detailed Process
Detailed Process
Sub Process
Detaild Process
Detailed Process
Overall Process
Start
End
Process
Recources Desission
Quality Desission
Rework

## Slide 18: Order Processing
Production Order
  Order new Robots
Manufacturing Order
  Produce basic parts. 3D print, laser cut, water-jet, miling, composite
Procurement Order
  Order to parts for the assemblies of a robot, a subsystem or components
Assembly Order
  Order to assemble a robot, a subsystem or parts
Warehouse Order
  Order to move something in the storage or get out of in. Or even move it from one storage to the other including commisioning
Shipment Order
  Order from customer to ship a robot
Recycling Order
  Order to recycle a robot or subsystems
Information Order
  To send or get Information about a certain product, process or equipment

## Slide 19: Order processing
https://help.sap.com/docs/SAP_INTEGRATED_BUSINESS_PLANNING/feae3cea3cc549aaa9d9de7d363a83e6/dedfcdc68f814333acab0763eb35bb01.html

## Slide 20: Naming, Serials and Tagging
Supports training and skills development for production staff. Tags can provide instructional information or guidance for handling specific parts or processes. Helps assess the effectiveness of training programs skills by tracking performance and handling of tagged parts.
RFID Tagging Robots and Sub-Systems
Robot Laser Coded QR, Data-Matrix-Code Tag on Baseplate including Robot Serial Number
Data Matrix Code or QR Code Tagging Components and Parts
Robot RFID-Tag on Base part of the Controller
Laser Engraved Code on Sensor boxes and Base parts for the Drive Systems
QR Code includes a Link to LCAM Platform
https://lcamp.eu/activity/an-open-innovation-community/?Serial=LCAMP-240912120212

## Slide 21: Overview LCAMP Configurator
Configurator.Core
Basic Classes
Configurator.Exporter
Library to Import-Export Robot
Configurator.Color
Scheme Mangement
LCAMP Configurator
Graphical User Inteface
LCAMP Process
Graphical Process Tool
STL Viewer
Tool to Manage STL Files
Import Robot Script
Export URDF Script
Configurator.Color
Scheme Mangement
LCAMP Configurator
Graphical User Inteface
Configurator.UI
Form Elements for Graphical User Interface
Export Part-List Script
Graphical Applications
CMD Applications (Scripts)
Libraries
Core Libraries

## Slide 22: ToDos Configurator
Configuration
Tree View with diferent Information
Devices  has Arduino code
Assemblies
Parts  Description and number of parts
Filter alowed Parts in configuration
Drive configurations
Sensor configurations
….
Structure parts in Versions (10 Different Types of Regular Wheel, Collor, Material, Dsign, ..)
Drive configurations
Sensor configurations
Relative Data Handling
Use Copied .stl-Files with relative Paths
Include Reset Structure to Template
Include Collor Scheme as Template and Reference to specific Robot
….
Part-List generation
Generate complete partlist
Include all C-Parts like screws and Cables
Generate flat partlist for Excel
Code Generation
Working partly  Test and optimize
Handling Variable Configuration with multi Sensors
Complete description of all Tools
Errorhandling for not existing or unusable partdescriptions

## Slide 23: ToDos Configurator Color
Color Scheme
Use Base Schem and Apply dynamic colors
Save individual Collorscheme and set to a Robot in Templates
Manage Color Schemes
…
Reference Colors to Materials

## Slide 24: ToDos Process
Generate Processes on Robot ConfigurationPart-List generation
Generate complete and detaild partlists for Processstep
Warehouse
List of available Parts
Generate missing Part Lists
Generate procurment orders, production prders or shiping orders

## Slide 25: ToDos STLViewer
Generate additional Information
Set Cooardinate Root System
generate Boundig Box
Generat Geometrey of CenterPoint
Generate Template for Part ( .stFile, Bounding Box, Genter of Gravity, Mass, Inertia)
STLViewer in LCAMP Viewer
Using Robot-Configuration
Change Part Templates
Calculate with Geometry
4x4 Matrix, Rotation and Trans-Sequence, Quarternions

## Slide 26: Software
https://apps.microsoft.com/detail/9nblggh42ths?hl=de-DE&gl=LI
Einfaches Anzeigen von 3D-Modellen und -Animationen in Echtzeit. 3D-Viewer können Sie 3D-Modelle mit Beleuchtungssteuerelementen anzeigen, Modelldaten untersuchen und verschiedene Schattierungsmodi visualisieren.
https://github.com/LCAMP-DHBW/LCAMP
Git Link für Konfigurator
https://github.com/LCAMP-DHBW/LCAMP_CONFIGURATOR

## Slide 27
www.lcamp.eu
@LCAMP_EU
LCAMP Learner Centric Advanced Manufacturing Platform for CoVEs